## Slide 1
Spoiled Beverage Detector
Solution Design in Medical Engineering
Medical Systems Engineering
Vanessa Mathew , Bahar Rahmani
Kymbat Talant , Jahangir Esfandiari

## Slide 2: Overview
Introduction
Current Technology
Functions & structures
Possible designs
Gas sensor
PH meter
Final design
Outlook
Biochemistry of Beverages

## Slide 3: Introduction
Consumption of spoiled drinks
Lack of awareness of early signs of expired drinks
Stomach cramp, fever, vomiting, nausea, diarrhea
Suspicious cases of beverage spoilage
Discarding
Boiling & cooling down (e.g. milk)
Waste of food, energy & time

## Slide 4: Introduction
Objective
Development of a device for fast detection of spoiled drinks & report of results

## Slide 5: Biochemistry
PH range of beverages
Juices | pH range | Mean
Orange | 4.19 - 4.50 | 4.34
Sweet lime | 4.70 - 5.47 | 5.08
Carrot | 5.76 - 6.03 | 5.89
Milk | 6.6-6.8 | 6.7
Table1: PH level of different drinks [1]

## Slide 6: Biochemistry
Spoiled beverage microorganisms
Microorganisms in spoiled beverage
Yeasts
Bacteria
Molds
Mycotoxins
Pathogens

## Slide 7: Current technologies
Media cup
Representing content information (e.g. temperature)
Fig.1. Media cup Prototypes,
Gellersen et al. International Symposium on Handheld and Ubiquitous Computing (1999)
Components
sensors
Microprocessor
capacitors
Infrared network
Software

## Slide 8: Current technologies
Vessyl
Fig.2. Vessyl smart cup,
http://hiconsumption.com/2014/06/vessyl-smart-cup/
Detecting amount & type of beverage
Information displayed on side of cup
Mobile App to track every sip
Indication of sufficient hydration by blue light

## Slide 9: Current technologies
Smart cap
Sensing quality of liquid in fluidic package
Fig.3. Design of a wireless “smart cap”, [5]
Based on changes in capacitance
Resonance frequency shifts of the LC tank via an inductive reader
LC tank as wireless-resonant sensor
Passive operation without power consumption

## Slide 10: Current technologies
Smart cap
Fig.4. (a) smart cap with milk package (b) LC resonant circuit, [5]

## Slide 11: Why Milk?
Selection of 1 type of drink to detect – Pasturized Milk
Easier to detect spoiled milk than spoiled juices
Spoiled juices have a wide range of pH value between different fruits
Health issues in third world countries
Human senses are often inadequate
Important nutrients for humans as wells as for animals

## Slide 12: Possible designs
Gas sensor
Fig.5. TGS 800 sensor,
https://ciiva.com/part/tgs-800-13645760
Use of a gas sensor TGS 800
Closed measuring chamber
Power Supply
Voltmeter

## Slide 13: Possible designs
Gas sensor
Fig.6. Enclosed Glass Box Drawing, done by Solid Works

## Slide 14: Possible designs
Gas sensor
Glass
Gas Sensors
Hole for Wiring
Spoiled Milk
Polymer
Fig.7. Enclosed Glass Box Drawing, done by Solid Works

## Slide 15: Final design
PH meter
Fig.8. Prototype of spoiled beverage detector
Rduino Microcontroller

## Slide 16: Final Design
Demonstration of healthy milk detection

## Slide 17: Final Design
Demonstration of sour milk detection

## Slide 18: Data Management and Blog

## Slide 19: Outlook
Method elaboration for detection
of other sorts of beverages
Shape & size optimization
Built-in programming
Attractive design
Marketing & commercializing opportunities

## Slide 20: References
[1] Alicyclobacillus spp. Control in the Fruit Juice Industry
[2] Microbiology of soft drinks and fruit juices (P. Wareing and R.R.) Davenport
[3] http://dairyprocessinghandbook.com/chapter/chemistry-milk
[4] Shinde Kajal P. et al IoT based detection of microbial activity in raw milk by using Intel Galileo Gen II in IRJET, india, 2017.
[5] Sung-Yueh Wu et al. 3D-printed microelectronics for integrated circuitry and passive wireless sensors in Microsystems & Nanoengineering, USA,2015
Fig.6.
[a] https://grabcad.com/library/circuit-board-pcb-mock-example
[b] https://grabcad.com/library/agian-glass-1

## Slide 21
Thanks for your attention!