## Slide 1
Spoiled Beverage Detector
Jahangir Esfandiari (ID:)
Rahmani Rahmani (ID:)
Kymbat Talant (ID:)
Vanessa Mathew (ID: 217957)

## Slide 2: Outline
Introduction/Objective
Current Technologies
Early Findings (fruit juices and milk)
Functions and structures
Possible Solutions : Option 1 (gas sensor)
Possible Solutions : Option 2 (pH meter)
Complete design status
Demonstration
Evaluation

## Slide 3: Introduction/Objective
Consuming Expired Drinks
Effect: Stomach cramp, fever, vomiting, nausea, diarrhea, etc
boiling milk takes time
Children not aware of the early signs of expired drinks
Objective: Smart cup should be developed in order to detect expired drinks and display the results fast.

## Slide 4: Current Technologies: Smart Cap
Sensing the quality of liquid in fluidic package
Based on changes in capacitance
Resonance frequency shifts of the LC tank via an inductive reader
LC tank as wireless-resonant sensor
Passive operation without power consumption
Fig.1. Design of a wireless “smart cap”
Sung-Yueh Wu et al. 3D-printed microelectronics for integrated circuitry and passive wireless sensors in Microsystems & Nanoengineering, USA,2015

## Slide 5: Current Technologies: Smart Cap (Design)
LC resonant circuit
Fig.2. (a) smart cap with milk package, (b) LC circuit diagram
Notes: By flipping the food package upside down. the liquid food is trapped inside the capacitor gap of the LC tank and acts as the dielectric
material. The LC tank’s fres, is determined by the dielectric constant of the liquid food.

## Slide 6: Current Technologies: Vessyl
Smart Cup  amount of liquid, type of beverage
Information on the side
Mobile app track every sip
Turns blue  Hydration
Only track water
Fig.3. Vessyl smart cup
http://hiconsumption.com/2014/06/vessyl-smart-cup/

## Slide 7: Current Technologies: Berkeley
Smart cup  track the consumption of common beverages
No detection of spoilage
LED on one side with sensor on the other side
Force resistor on the bottom of the cup
Wireless device in the base
App in mobile device

## Slide 8: Current Technologies: Media Cup
Coffee Cup  Represent the context information: Location, Temperature
Components
Acceleration sensor
Microcontroller
Infrared diode
Lithium Battery
Semiconductor chip
Overhead Transceiver
Fig.4. Media cup Prototypes
Hans-W. Gellersen et al. The MediaCup: Awareness Technology embedded in an Everyday Object in Telecooperation office, Karlsruhe, Germany, 2001
Notes: first version for initial data collection but was not fit for day-to-day use.
second prototype embedded the MediaCup hardware at the bottom of a coffee cup.
third prototype  the hardware mounted in the rubber base of the HUC99 coffee cup, allowing removal so that the cup can be dishwashed.

## Slide 9: Early Findings: Fruit Juices Property
Fruit juices have pH in the acidic range (<4.5) serving as important barrier for microbial growth
Freshly expressed juice, is highly susceptible to spoilage more than whole fruit
Juices | pH range | Mean
Orange | 4.19–4.50 | 4.34
Sweet lime | 4.70–5.47 | 5.08
Carrot | 5.76–6.03 | 5.89
Table1: PH level of different fruit juices [1]
Notes: Source: Alicyclobacillus spp. Control in the Fruit Juice Industry
Microbiology of soft drinks and fruit juices (P. Wareing and R.R.) Davenport
-Unprotected by skin or cell walls, fluid components are thoroughly mixed with air and microorganisms from the environment.

## Slide 10: Early Findings: Critical factors affecting the spoilage of juices
Effects:
Cloud loss
Development of off-flavors
CO2 production
Changes in color, texture, and appearance
Intrinsic | Extrinsic
Juice pH | storage temperatures and times
Water activity | relative humidity conditions during storage and packaging material characteristics.
Table2: Intrinsic & Extrinsic Properties for Juice Spoilage [2]
Notes: Source: Microbiology of soft drinks and fruit juices (P. Wareing and R.R.) Davenport

## Slide 11: Motivation for detecting spoiled milk
Important nutrients for humans as wells as for animals
Good milk wastage
Health issues in third world countries
Human senses are often inadequate
Solution: Smart sensing ph-system to make on time descisions

## Slide 12: Composition of cow‘s milk
The pH value of normal milk is in the range between 6.6-6.8 at 25°C
Main constituent | Limits of variation | Mean value
Water | 85.5 – 89.5 | 87.5
Total solids | 10.5 – 14.5 | 13.0
Fat | 2.5 – 6.0 | 3.9
Proteins | 2.9 – 5.0 | 3.4
Lactose | 3.6 – 5.5 | 4.8
Minerals | 0.6 – 0.9 | 0.8
Table3: Quantitative composition of milk [3]

## Slide 13: Different milk properties
Raw Milk | A wide variety of germs
Pasteurized Milk | Coxiella burnetti, Poreformers, Listeria Monocytogenes, Coliforms.
Condensed Milk | Glaucus, Aspergillus repens, Torulopsis.
Dried Milk | Bacillus, Micrococcus, Mucor
Table 4: Milk forms [4]

## Slide 14: Early Findings: Fruit Juices + Milk Microorganisms
Fruit juices contain a microflora which is normally present on the surface of fruits during harvest and postharvest processing which include transport, storage, and processing.
Common pathogens/bacteria seen both in milk and juice: Salmonella, E. coli., Pseudomonas
Microorganisms in spoiled fruit juices
Yeasts
Bacteria
Molds
Mycotoxins
Pathogens
Notes: Source: - Emerging Preservation Techniques for Controlling Spoilage and Pathogenic Microorganisms in Fruit Juices
Microbes Associated with Freshly Prepared Juices of Citrus and Carrots
However, food borne pathogens such as E. coli and Salmonella survive in acidic environment of fruit juices due to acid stress response

## Slide 15: Optrion1 – Gas sensor
Use of a gas sensor TGS 800
Closed measuring chamber
Power Supply
Voltmeter
Fig.5. TGS 800 sensor
https://ciiva.com/part/tgs-800-13645760

## Slide 16: Option 1 (Gas Sensor)
Fig.6. : Enclosed Vacuum Glass Box
Drawing: Arduino Part [a] , Cup Part [b]
Drawing assembled by Vanessa.M

## Slide 17: Option 1 (Gas Sensor)
Fig.7. Enclosed Vacuum Glass Box
Drawing: Arduino Part [a] , Cup Part [b]
Drawing assembled by Vanessa.M

## Slide 18: Option 1 (Gas Sensor)
Fig.8.Enclosed Vacuum Glass Box
Drawing: Arduino Part [a] , Cup Part [b]
Drawing assembled by Vanessa.M
Glass
Gas Sensors
Hole for Wiring
Spoiled Milk
Polymer

## Slide 19: References
[1] Alicyclobacillus spp. Control in the Fruit Juice Industry
[2] Microbiology of soft drinks and fruit juices (P. Wareing and R.R.) Davenport
[3] http://dairyprocessinghandbook.com/chapter/chemistry-milk
[4] Shinde Kajal P. et al IoT based detection of microbial activity in raw milk by using Intel Galileo Gen II in IRJET, india, 2017.
Fig.6.:
[a] https://grabcad.com/library/circuit-board-pcb-mock-example
[b] https://grabcad.com/library/agian-glass-1